## Slide 1
Stephen Ibanez, Noa Zilberman, Robert Halstead, Sean Choi, Gianni Antichi
Tutorial

## Slide 2: Outline
NetFPGA Overview
P4->NetFPGA Workflow Overview
Tutorial Assignments

## Slide 3: Overview

## Slide 4
Section I: The NetFPGA platform

## Slide 5: NetFPGA = Networked FPGA
A line-rate, flexible, open networking platform for teaching and research

## Slide 6
NetFPGA Family of Boards
NetFPGA-1G (2006)
NetFPGA-1G-CML (2014)
NetFPGA-10G (2010)
NetFPGA SUME (2014)

## Slide 7: NetFPGA consists of…
Four elements:
NetFPGA board
Tools + reference designs
Contributed projects
Community

## Slide 8: NetFPGA board
PC with NetFPGA
Networking Software
running on a standard PC
A hardware accelerator
built with Field Programmable Gate Array driving 1/10/
100Gb/s network links
FPGA
Memory
10GbE
10GbE
10GbE
10GbE
PCI-Express
CPU
Memory

## Slide 9: Tools + Reference Designs
Tools:
Compile designs
Verify designs
Interact with hardware
Reference designs:
Router (HW)
Switch (HW)
Network Interface Card (HW)
Router Kit (SW)
SCONE (SW)

## Slide 10: Community
Wiki
Documentation
    User’s Guide “so you just got your first NetFPGA”
    Developer’s Guide “so you want to build a …”
Encourage users to contribute
Forums
Support by users for users
Active community - 10s-100s of posts/week

## Slide 11: International Community
Over 1,200 users, using over 3500 cards at
200 universities in over 47 countries

## Slide 12: NetFPGA’s Defining Characteristics
Line-Rate
  Processes back-to-back packets
    Without dropping packets
    At full rate
  Operating on packet headers
    For switching, routing, and firewall rules
  And packet payloads
    For content processing and intrusion prevention
Open-source Hardware
  Similar to open-source software
    Full source code available
    BSD-Style License for SUME, LGPL 2.1 for 10G
  But harder, because
    Hardware modules must meet timing
    Verilog & VHDL Components have more complex interfaces
    Hardware designers need high confidence in specification of modules

## Slide 13: Test-Driven Design
Regression tests
  Have repeatable results
  Define the supported features
  Provide clear expectation on functionality
Example: Internet Router
  Drops packets with bad IP checksum
  Performs Longest Prefix Matching on destination address
  Forwards IPv4 packets of length 64-1500 bytes
  Generates ICMP message for packets with TTL <= 1
  Defines how to handle packets with IP options or non IPv4
    … and dozens more … Every feature is defined by a regression test

## Slide 14: Who, How, Why
Who uses the NetFPGA?
  Researchers
  Teachers
  Students
How do they use the NetFPGA?
  To run the Router Kit
  To build modular reference designs
    IPv4 router
    4-port NIC
    Ethernet switch, …
Why do they use the NetFPGA?
  To measure performance of Internet systems
  To prototype new networking systems

## Slide 15
Section II: Hardware Overview

## Slide 16: NetFPGA-SUME

## Slide 17: NetFPGA-SUME
High Level Block Diagram

## Slide 18: Xilinx Virtex 7 690T
Optimized for high-performance applications
690K Logic Cells
52Mb RAM
3 PCIe Gen. 3 Hard cores

## Slide 19: Memory Interfaces
DRAM: 2 x DDR3 SoDIMM 1866MT/s, 4GB
SRAM: 3 x 9MB QDRII+, 500MHz

## Slide 20: Host Interface
PCIe Gen. 3
x8 (only)
Hardcore IP

## Slide 21: Front Panel Ports
4 SFP+ Cages
Directly connected to the FPGA
Supports 10GBase-R transceivers (default)
Also Supports 1000Base-X transceivers and direct attach cables

## Slide 22: Expansion Interfaces
FMC HPC connector
  VITA-57 Standard
  Supports Fabric Mezzanine Cards (FMC)
  10 x 12.5Gbps serial links
QTH-DP
  8 x 12.5Gbps serial links

## Slide 23: Storage
128MB FLASH
2 x SATA connectors
Micro-SD slot
Enable standalone operation

## Slide 24: Beyond Hardware
NetFPGA Board
Xilinx Vivado based IDE
Reference designs using AXI4
Software (embedded and PC)
Public Repository
Public Wiki
Reference Designs
AXI4 IPs
Xilinx Vivado
MicroBlaze SW
PC SW
GitHub, User Community

## Slide 25
Integrated Circuit Technology
And Field Programmable Gate Arrays (FPGAs)

## Slide 26: Integrated Circuit Technology
Full-custom Design
  Complementary Metal Oxide Semiconductor (CMOS)
Semi-custom ASIC Design
  Gate array
  Standard cell
Programmable Logic Device
  Programmable Array Logic
  Field Programmable Gate Arrays
Processors

## Slide 27
LUT/RAM/SRL
LUT/RAM/SRL
LUT/RAM/SRL
LUT/RAM/SRL
0 1
FF/L
FF
Xilinx Virtex-7
Diagram From: Xilinx, Inc.
Logic Resources
Memory resources
Macro blocks
Clocking resources
Routing resources
I/O resource
….
A program is limited by the available resources
A program keeps running:
  Until reprogrammed
  Until a power cycle

## Slide 28
Section III: Life of a Packet

## Slide 29: Reference Switch Pipeline
Five stages
  Input port
  Input arbitration
  Forwarding decision and packet modification
  Output queuing
  Output port
Packet-based module interface
Pluggable design
10GE
RxQ
10GE
RxQ
10GE
RxQ
10GE
RxQ
DMA
Input Arbiter
Output Port Lookup
Output Queues
10GE
Tx
10GE
Tx
10GE
Tx
10GE
Tx
DMA

## Slide 30: Full System Components
Software
PCIe Bus
NetFPGA
Application
Driver
AXI Lite
user data path
DMA
Registers
nf0
nf1
nf2
nf3
ioctl
MAC
TxQ
MAC
RxQ
Ports
CPU
RxQ
CPU
TxQ
MAC
TxQ
MAC
RxQ
MAC
TxQ
MAC
RxQ
10GE
Tx
10GE
Rx

## Slide 31: Life of a Packet through the Hardware
00:0a:..:0X
00:0a:..:0Y
ETH packet
Port 1
Port 2

## Slide 32: 10GE Rx Queue
10GE Rx Queue
Eth Hdr:
Dst MAC,
Src MAC
Data

## Slide 33: 10GE Rx Queue
10GE Rx Queue
Eth Hdr:
Dst MAC, Src MAC
Payload
Length, Src port, Dst port, User defined
0
TUSER
TDATA

## Slide 34: Input Arbiter
Input Arbiter
Rx
0
Rx
1
…
Rx
4
Pkt
Pkt
Pkt

## Slide 35: Output Port Lookup
Output Port Lookup
Packet Header
Payload
Length, Src port, Dst port, User defined
0

## Slide 36: Output Queues
Output Queues
Pkt
OQ0
OQ2
OQ4

## Slide 37: 10GE Port Tx
10GE Port Tx
Eth Hdr: Dst MAC , Src MAC
Payload
Length, Src port, Dst port, User defined
0

## Slide 38: MAC Tx Queue
MAC Tx Queue
Eth Hdr: Dst MAC , Src MAC
Payload
Length, Src port, Dst port, User defined
0

## Slide 39: NetFPGA-Host Interaction
Linux driver interfaces with hardware
  Packet interface via standard Linux network stack
  Register reads/writes via ioctl system call with wrapper functions:
    rwaxi(int address, unsigned *data);
    eg:
    rwaxi(0x7d4000000, &val);
Notes: Named registers are flakey

## Slide 40: NetFPGA-Host Interaction
NetFPGA to host packet transfer
PCIe Bus
2. Interrupt notifies driver of packet arrival
3. Driver sets up and initiates DMA transfer
1. Packet arrives – forwarding table sends to DMA queue

## Slide 41: NetFPGA-Host Interaction
NetFPGA to host packet transfer (cont.)
PCIe Bus
4. NetFPGA transfers packet via DMA
5. Interrupt signals completion of DMA
6. Driver passes packet to network stack

## Slide 42: NetFPGA-Host Interaction
Host to NetFPGA packet transfers
PCIe Bus
3. Interrupt signals completion of DMA
1. Software sends packet via network sockets Packet delivered to driver
2. Driver sets up and initiates DMA transfer

## Slide 43: NetFPGA-Host Interaction
Register access
PCIe Bus
1. Software makes ioctl call on network socket ioctl passed to driver
2. Driver performs PCIe memory read/write

## Slide 44: P4->NetFPGA Workflow Overview

## Slide 45: General Process for Programming a P4 Target
NetFPGA SUME
P4->NetFPGA tools
SimpleSumeSwitch
Architecture
Notes: So here is the general process for programming a P4 target.
The manufacturer of the target provides the P4 programmer with 3 things
  The target itself
  A compiler that takes in the P4 program and generates the data-plane runtime implementation for the target, as well as an API to allow the control plane to interact with the tables and other stateful elements in the data-plane
  The manufacturer also provides a P4 architecture model for their target that the user then instantiates with their P4 program.
Target = NetFPGA
P4 compiler = P4->NetFPGA Workflow

## Slide 46: P4->NetFPGA Compilation Overview
P4 Program
Xilinx P416 Compiler
Xilinx SDNet Tools
SSS
SimpleSumeSwitch Architecture
NetFPGA Reference Switch

## Slide 47: SimpleSumeSwitch Architecture Model for SUME Target
P4 used to describe parser, match-action pipeline, and deparser
tdata
AXI
Lite
tdata
AXI
Lite
tuser
tuser
Notes: Here is the particular P4 architecture model that we are currently using for the SUME target, which we are calling the SimpleSumeSwitch architecture because it is pretty much the most basic thing that we could do.
As you can see, it consists of …
The P4 programmer is responsible for filling in the implementation of the parser, match-action pipeline, and deparser with their P4 program
Name buses – axi_stream, axi_lite

## Slide 48: Metadata in SimpleSumeSwitch Architecture
/* standard sume switch metadata */
struct sume_metadata_t {
bit<16> dma_q_size;
bit<16> nf3_q_size;
bit<16> nf2_q_size;
bit<16> nf1_q_size;
bit<16> nf0_q_size;
bit<8> send_dig_to_cpu; // send digest_data to CPU
bit<8> drop;
bit<8> dst_port; // one-hot encoded
bit<8> src_port; // one-hot encoded
bit<16> pkt_len; // unsigned int
}
*_q_size – size of each output queue, measured in terms of 32-byte words, when packet starts being processed by the P4 program
src_port/dst_port – one-hot encoded, easy to do multicast
user_metadata/digest_data – structs defined by the user
Notes: Here is the current definition of the standard SUME metadata bus
This bus consists of the fields that are set or used by other parts of the switch architecture outside of the parser, match-action pipeline, and deparser
It consists of things like …

## Slide 49: SimpleSumeSwitch vs. V1 Model
/* standard sume switch metadata */
struct sume_metadata_t {
bit<16> dma_q_size;
bit<16> nf3_q_size;
bit<16> nf2_q_size;
bit<16> nf1_q_size;
bit<16> nf0_q_size;
bit<8> send_dig_to_cpu;
bit<8> drop;
bit<8> dst_port;
bit<8> src_port;
bit<16> pkt_len;
}
/* standard V1 switch metadata* */
struct standard_metadata_t {
bit<32> enq_timestamp;
bit<32> deq_timedelta;
bit<19> enq_qdepth;
bit<19> deq_qdepth;
bit<9> egress_port;
bit<32> clone_spec;
bit<1> drop;
bit<9> egress_spec;
bit<9> ingress_port;
bit<32> packet_length;
bit<32> instance_type;
bit<16> recirculate_port;
bit<48> ingress_global_timestamp;
bit<32> lf_field_list;
bit<16> mcast_grp;
bit<1> resubmit_flag;
bit<16> egress_rid;
}
*reordered for alignment
Notes: - Here is a comparison of the standard metadata fields in the SimpleSumeSwitch and the V1 model
- As you can see there is some

## Slide 50: Overall P4 Program Structure
#include <core.p4>
#include <sume_switch.p4>
/******** CONSTANTS ********/
#define IPV4_TYPE 0x0800
/******** TYPES ********/
typedef bit<48> EthAddr_t;
header Ethernet_h {...}
struct Parsed_packet {...}
struct user_metadata_t {...}
struct digest_data_t {...}
/******** EXTERN FUNCTIONS ********/
extern void const_reg_rw(...);
/******** PARSERS and CONTROLS ********/
parser TopParser(...) {...}
control TopPipe(...) {...}
control TopDeparser(...) {...}
/******** FULL PACKAGE ********/
SimpleSumeSwitch(TopParser(), TopPipe(), TopDeparser()) main;

## Slide 51: Externs
Implement platform specific functions
    Black box to P4 program
Stateless – reinitialized for each packet
Stateful – keep state between packets
Xilinx Annotations
    @Xilinx_MaxLatency() – maximum number of clock cycles an extern function needs to complete
    @Xilinx_ControlWidth() – size in bits of the address space to allocate to an extern function

## Slide 52: P4->NetFPGA Extern Function Library
HDL modules invoked from within P4 programs
Stateful Atoms
  Stateless Externs
  Add your own!
Atom | Description
R/W | Read or write state
RAW | Read, add to, or overwrite state
PRAW | Predicated version of RAW
ifElseRAW | Two RAWs, one each for when predicate is true or false
Sub | IfElseRAW with stateful subtraction capability
Atom | Description
IP Checksum | Given an IP header, compute IP checksum
LRC | Longitudinal redundancy check, simple hash function
timestamp | Generate timestamp (granularity of 5 ns)
Notes: - Extern implementations must be able to accept data on every clock cycle, so they must be pipelined if they take more than 1 clock cycle to complete.

## Slide 53: Using Atom Externs in P4 – Resetting Counter
Packet processing pseudo code:
count[NUM_ENTRIES];
if (pkt.hdr.reset == 1):
count[pkt.hdr.index] = 0
else:
count[pkt.hdr.index]++

## Slide 54: Using Atom Externs in P4 – Resetting Counter
#define REG_READ 0
#define REG_WRITE 1
#define REG_ADD 2
// count register
@Xilinx_MaxLatency(1)
@Xilinx_ControlWidth(3)
extern void count(in bit<3> index,
in bit<32> newVal,
in bit<32> incVal,
in bit<8> opCode,
out bit<32> result);
bit<16> index = pkt.hdr.index;
bit<32> newVal;
bit<32> incVal;
bit<8> opCode;
if(pkt.hdr.reset == 1) {
newVal = 0;
incVal = 0; // not used
opCode = REG_WRITE;
} else {
newVal = 0; // not used
incVal = 1;
opCode = REG_ADD;
}
bit<32> result; // the new value stored in count
count_reg_raw(index, newVal, incVal, opCode, result);
State can be accessed exactly 1 time
Using RAW atom here
Instantiate atom
Set metadata for state access
Single state access!

## Slide 55: P4-NetFPGA Workflow
Write P4 program
Write python gen_testdata.py script
Compile to verilog / generate API & CLI tools
    $ make
Run initial SDNet simulation
    $ ./vivado_sim.bash
Install SDNet output as SUME library core
    $ make install_sdnet
Run NetFPGA simulation
    $ ./nf_test sim –major switch –minor default
Build bitstream
    $ make
Test the hardware
All of your effort will go here
Notes: Tools to help write testdata
  sss_sdnet_tuples
  scapy
Tools to help debug failing simulations
  Parsing simulation output into header / metadata fields

## Slide 56: Directory Structure of $SUME_FOLDER
P4-NetFPGA-SIGCOMM/
|
|- contrib-projects/
| |- sume-sdnet-switch/  the main directory for P4 dev
|
|- lib/  contains all of the SUME IP cores
|
|- tools/  various NetFPGA scripts for test infra.
|
|- Makefile  builds all of the SUME IP cores

## Slide 57: Directory Structure of $SUME_SDNET
sume-sdnet-switch/
|
|- bin/  scripts used to automate workflow
|
|- templates/  templates for externs, wrapper module,
| CLI tools, new projects
|
|- projects/  all of the P4 project directories
| |- switch_calc/

## Slide 58: Directory Structure of $P4_PROJECT_DIR
$P4_PROJECT_DIR/
|
|- src/  P4 source files and commands.txt
|
|- testdata/  scripts to generate testdata used for
| verifying functionality of P4 program
|
|- simple_sume_switch/  main SUME project directory,
| top level HDL files and SUME sim scripts
|
|- sw/  populated with API files and CLI tools and any
| user software for the project
|
|- nf_sume_sdnet_ip/  SDNet output directory

## Slide 59: API & Interactive CLI Tool Generation
Both Python API and C API
    Manipulate tables and stateful elements in P4 switch
    Used by control-plane program
  CLI tool
    Useful debugging feature
    Query various compile-time information
    Interact directly with tables and stateful elements in real time

## Slide 60: Debugging P4 Programs
SDNet HDL simulation
SDNet C++ simulation
    Verbose packet processing info
    Output PCAP file
Full SUME design HDL simulation

## Slide 61: What can you do in 2.5 days?
Examples from the recent NetFPGA Summer Camp:
    Heavy hitter detection
    Event triggered network monitor
    Packet Fuzzer
    Tic-Tac-Toe

## Slide 62: Get the Tools!
Fill out P4->NetFPGA github registration form: here
Request P4->NetFPGA tools and licenses from Xilinx: here
    P4-SDNet License
    Vivado license
    10G MAC Core license
(For academic users) Request special price NetFPGA SUME: here
(For industry users) Purchase NetFPGA SUME from Digilent: here
Read the documentation: here

## Slide 63: Today’s Development Process
Google Compute Instance:
    P4 development
    P4 -> HDL compilation
    Simulation + debugging
    Bitstream generation
Hardware Test Machines:
    Testing on SUME boards
  Connecting to machines:
    Use “p4-netfpga-ssh-key”
    Command line development OR VNC client

## Slide 64: Tutorial Assignments

## Slide 65: Tutorial Assignments
Assignments described at this link:
    https://github.com/NetFPGA/P4-NetFPGA-public/wiki/Tutorial-Assignments
Short version:
    https://tinyurl.com/P4-NetFPGA-SIGCOMM-17

## Slide 66: Assignment 1: Switch as a Calculator

## Slide 67: Switch as Calculator
Supported Operations:
ADD – add two operands
SUBTRACT – subtract two operands
ADD_REG – add operand to current value in register
SET_REG – overwrite the current value of the register
LOOKUP – Lookup the given key in the table
header Calc_h {
bit<32> op1;
bit<8> opCode;
bit<32> op2;
bit<32> result;
}

## Slide 68: Switch as Calculator
DST: MAC1
SRC: MAC2
Type: CALC_TYPE
Ethernet
Calc
Payload…
User PC
NetFPGA SUME
op1: 1
opCode: ADD
op2: 2
result: 0

## Slide 69: Switch as Calculator
DST: MAC1
SRC: MAC2
Type: CALC_TYPE
Ethernet
Calc
Payload…
User PC
NetFPGA SUME
op1: 1
opCode: ADD
op2: 2
result: 0 3
X

## Slide 70: Switch as Calculator
DST: MAC2
SRC: MAC1
Type: CALC_TYPE
Ethernet
Calc
Payload…
User PC
NetFPGA SUME
op1: 1
opCode: ADD
op2: 2
result: 3

## Slide 71: Switch Calc Operations
ADD
result
op1 op2
+
SUB
result: op1-op2
op1 op2
-
ADD_REG
result
op2 const[op1]
+
SET_REG
const[op1]
op2
LOOKUP
result:
val
key:
op1
key | val
0 | 1
1 | 16
2 | 162
3 | 163

## Slide 72: Assignment 2: TCP Monitor

## Slide 73: TCP Monitor
Practice writing stateful P4 programs for NetFPGA SUME
Compute TCP flow size distribution in the data-plane
Flow is determined by 5-tuple and delimited by SYN/FIN
Fine grained flow monitoring capabilities with P4
Flow Size (bytes)
# Flows
Flow Size Distribution

## Slide 74
0
0
0
0
0
0
0
0
0
0-16K
16-32K
32-48K
48-64K
64-80K
80-96K
96-112K
>112K
hash
Ethernet
IP_src
IP_dst
Proto: TCP
sport
dport
flags: SYN
byte_cnt
distribution

## Slide 75
0
hash
byte_cnt
Ethernet
IP_src
IP_dst
Proto: TCP
sport
dport
flags: ACK
len(payload) = 1K
1K
0
0
0
0
0
0
0
0
0-16K
16-32K
32-48K
48-64K
64-80K
80-96K
96-112K
>112K
distribution

## Slide 76
0
0
0
0
0
0
0
0
0-16K
16-32K
32-48K
48-64K
64-80K
80-96K
96-112K
>112K
distribution
1K
hash
byte_cnt
Ethernet
IP_src
IP_dst
Proto: TCP
sport
dport
flags: FIN
len(payload) = 1K
2K
1

## Slide 77: Assignment 3: In-band Network Telemetry (INT)

## Slide 78: In-band Network Telemetry (INT)
One of the most popular applications for programmable data-planes
All about gaining more visibility into network
Basic idea:
    Source requests each switch along path to insert some desired metadata into packet (using a bitmask)
  Example metadata:
    Switch ID
    Ingress Port
    Egress Port
    Timestamp
    Queue Occupancy

## Slide 79: In-band Network Telemetry (INT)
Ethernet
INT
bm: 11001
SwitchID
Payload
Ingress port
timestamp
    Bitmask format (5 bits):
    <SWITCH_ID><INGRESS_PORT><Q_SIZE><TSTAMP><EGRESS_PORT>
Queue size
Egress port

## Slide 80: In-band Network Telemetry (INT)
Ethernet
INT
bm: 11001
SwitchID
Payload
Ingress port
timestamp
    Bitmask format (5 bits):
    <SWITCH_ID><INGRESS_PORT><Q_SIZE><TSTAMP><EGRESS_PORT>
Queue size
Egress port
SwitchID
bos: 0
Ingress port
bos: 0
Egress port
bos: 1

## Slide 81: Additional Details
Notes: Now I’ll briefly describe the process of compiling P4 programs using the Xilinx P4-SDNet toolchain
But before I do, I want to clarify that P4-SDNet is an official Xilinx product, so I haven’t had much to do with it’s development other than helping to debug a few features here and there
I was just fortunate enough to get the opportunity to put it to use for NetFPGA

## Slide 82: API
Auto generated Python API
Exact match table API functions:
    table_cam_add_entry()
    table_cam_delete_entry()
    table_cam_get_size()
    table_cam_read_entry()
Ternary match table API functions:
    table_tcam_add_entry()
    table_tcam_clean()
    table_tcam_erase_entry()
    table_tcam_verify_entry()
LPM table API functions:
    table_lpm_load_dataset()
    table_lpm_set_active_lookup_bank()
    table_lpm_verify_dataset()
  Register API functions:
    reg_read()
    reg_write()
  C API also available

## Slide 83: Implementing Extern Functions
Implement verilog extern module in $SUME_SDNET/templates/externs/
Add entry to $SUME_SDNET/bin/extern_data.py
No Need to modify any existing code
If the extern has a control interface a cpu_regs module will be generated automatically to easily expose control_registers using the AXI Lite interface

## Slide 84: Debugging SDNet Simulation
HDLSimulation
    Xsim or Questa sim
    Error:
expected < tuple_out_sume_metadata > = < 00000000000000000000000100040041 >
actual < tuple_out_sume_metadata > = < 00000000000000000000000100040040 >
$ $P4_PROJECT_DIR/testdata/sss_sdnet_tuples.py --parse 00000000000000000000000100040041 sume
Parsed Tuple:
-----------------------
dma_q_size = 0
nf3_q_size = 0
nf2_q_size = 0
nf1_q_size = 0
nf0_q_size = 0
send_dig_to_cpu = 0
drop = 1
dst_port = 00000000
src_port = 00000100
pkt_len = 65

## Slide 85: Debugging SDNet Simulation
C++ model
    Prints debug info
      Hit or miss in tables
      Header/Metadata field modification along the way
    Generates Packet_expect.pcap to compare to dst.pcap
-skipEval option
    Compare C++ model output to HDL simulation – make sure SDNet compiler is working properly

## Slide 86: Debugging SUME Simulation
What to do if SDNet simulation passes but SUME simulation fails?
    Make sure you’ve:
      $ cd $P4_PROJECT_DIR && make config_writes
      $ cd $NF_DESIGN_DIR/test/sim_major_minor && make
      $ cd $P4_PROJECT_DIR && make install_sdnet
    Run SUME simulation longer?
    Make sure all configuration writes have completed before applying the test packets
    Make sure SDNet module has finished reset before applying configuration writes
    Check nf_*_expected.axi and nf_*_logged.axi
    Add signals to simulation waveform
    Perhaps issue with wrapper module?

## Slide 87: SDNet Module HDL Wrapper
Located in: $SUME_SDNET/templates/sss_wrapper/
Tasks:
    Generate tuple_in_VALID signal for s_axis_tuser
    Reverse reset polarity
    Reverses endianness of digest_data and inserts into last 80 bits of m_axis_tuser

## Slide 88: Acknowledgments (I)
Nick McKeown, Glen Gibb, Jad Naous, David Erickson, G. Adam Covington, John W. Lockwood, Jianying Luo, Brandon Heller, Paul Hartke, Neda Beheshti, Sara Bolouki, James Zeng, Jonathan Ellithorpe, Sachidanandan Sambandan, Eric Lo, Stephen Gabriel Ibanez
NetFPGA Team at Stanford University (Past and Present):
NetFPGA Team at University of Cambridge (Past and Present):
Andrew Moore, David Miller, Muhammad Shahbaz, Martin Zadnik, Matthew Grosvenor, Yury Audzevich, Neelakandan Manihatty-Bojan, Georgina Kalogeridou, Jong Hun Han, Noa Zilberman, Gianni Antichi, Charalampos Rotsos, Hwanju Kim, Marco Forconesi, Jinyun Zhang, Bjoern Zeeb, Robert Watson, Salvator Galea, Marcin Wojcik, Diana Andreea Popescu, Murali Ramanujam
All Community members (including but not limited to):
Paul Rodman, Kumar Sanghvi, Wojciech A. Koszek, Yahsar Ganjali, Martin Labrecque, Jeff Shafer, Eric Keller, Tatsuya Yabe, Bilal Anwer, Yashar Ganjali, Martin Labrecque, Lisa Donatini, Sergio Lopez-Buedo , Andreas Fiessler, Robert Soule, Pietro Bressana, Yuta Tokusashi
Patrick Lysaght, Kees Vissers, Michaela Blott, Shep Siegel, Cathal McCabe
Steve Wang, Erik Cengar, Michael Alexander, Sam Bobrowicz, Garrett Aufdemberg,
Patrick Kane, Tom Weldon

## Slide 89: Acknowledgements (II)